## Slide 1
Healthy Building Systems: Energy, Moisture & Materials
Course Number: AIAAEC_081415
Susan Doll & Lee Ball
Date: August 14, 2015
Appalachian State University
Provider Number: 60114136

## Slide 2
7 LU|HSW Credits earned on completion of this course will be reported to AIA CES for AIA members. Certificates of Completion for both AIA members and non-AIA members will be received at the end of the class.
This course is registered with AIA CES for continuing professional education. As such, it does not include content that may be deemed or construed to be an approval or endorsement by the AIA of any material of construction or any method or manner of handling, using, distributing, or dealing in any material or product.
_______________________________________
Questions related to specific materials, methods, and services will be addressed at the conclusion of this presentation.

## Slide 3
Course
Description
 | As building envelopes have become tighter to save energy and meet the changes required by the new NC Building Code, it is important to understand the potential impact of energy efficiency on indoor environment quality (IEQ). Tighter buildings can trap moisture resulting in mold growth, and inadequate ventilation leads to elevated contaminant concentrations, that may impact occupant health. This workshop will cover an integrated approach to building performance that explains the relationship between energy and IEQ, and how construction methods, materials, building pressure differences and airflow patterns influence moisture and contaminant generation/removal rates that ultimately determine the quality of indoor environments and health of building occupants. Participants will learn about observational diagnostic techniques and energy rating systems, and demonstrations will include IEQ monitoring methods and interpretation of results, that can be used to assess energy, moisture, and material related issues in existing buildings.

## Slide 4
Learning
Objectives
Understand how basic building science and construction techniques can affect indoor environment quality (IEQ) and may impact health of building occupants.
Review energy-efficiency measures outlined in the North Carolina Building Code and understand the inter-relationship with IEQ.
Participants will be able to identify design strategies that have the potential to enhance IEQ while maintaining energy efficiency objectives.
Participants will learn how to identify sources of air leakage through the use of diagnostic equipment.
At the end of the this course, participants will be able to:

## Slide 5: Workshop Agenda
INTRODUCTIONS
PART 1: The Indoor Environment
PART 2: Buildings as a System
<Break for lunch 12-1pm>
PART 3: Keeping Homes Healthy
PART 4: Smart Energy Practices
PART 5: Practical Applications, Q & A

## Slide 6: PART 1: The Indoor Environment
Dr. Susan Doll

## Slide 7
SHOULD…
Protect from elements (wind, rain)
Protect from animals and pests
Keep us warm in winter
Comfortable in summer
Accommodate occupant activities
SHOULD NOT…
Wreck the planet
Drive us to the poor house
Cause discomfort
Make us sick
The Built Environment

## Slide 8: BUILT ENVIRONMENT
UNCONDITIONED
(attic)
(basement, crawlspace)
(garage)
INDOOR ENVIRONMENT
(conditioned living space)
OUTDOORS
– Exterior, Boundary, Interior Space

## Slide 9: “TIGHTNESS” of Envelope
No Exchange =>
Completely Open

## Slide 10
  Mainly to improve energy efficiency
  Reduced air leakage around doors and windows
  Seal openings in walls, floors and ceilings
  Improve insulation to reduce thermal loss
Tight Buildings

## Slide 11: BUILT ENVIRONMENT
UNCONDITIONED
(attic)
(basement, crawlspace)
(garage)
INDOOR ENVIRONMENT
(conditioned living space)
OUTDOORS
– Exterior, Boundary, Interior Space - Airflow Quality, Magnitude, Direction

## Slide 12: BUILT ENVIRONMENT
UNCONDITIONED
(attic)
(basement, crawlspace)
(garage)
INDOOR ENVIRONMENT
(conditioned living space)
OUTDOORS
SYSTEMS
MATERIALS
OCCUPANTS
++++
+++
++
++++
+++
++
+++
++++
++++
++++
++++
+
+
+
+
++
+
+++
– Exterior, Boundary, Interior Space - Airflow Quality, Magnitude, Direction - Contaminant Type, Source, Strength

## Slide 13: IAQ vs. IEQ
  Indoor Air Quality
    Makeup of airborne substances
    Gases, chemicals, particles
    Allergens
  Indoor Environment Quality
    Occupant experience of the indoors
    Includes IAQ, thermal comfort, drafts
    Noise, lighting

## Slide 14
Thermal Comfort

## Slide 15: Dew Point - condensation
Warm air holds more moisture per volume
As air cools, moisture condenses
Moist air condenses on cold surfaces

## Slide 16
Air Quality
  Gases
  Chemicals/fumes (VOCs)
  Particulates
  Allergens
Thermal Comfort
  Temperature
  Humidity
INTERACTION
??

## Slide 17
How do thermal comfort parameters impact IAQ?
Occupant Material
Comfort Integrity Contaminants
Temp X + Offgassing
Humidity X -- Allergens (dust mites)
Dew Point --- X (mold)

## Slide 18
Air Quality
  Gases
  Chemicals/fumes (VOCs)
  Particulates
  Allergens
Thermal Comfort
  Temperature
  Humidity
Occupants
Building/Systems
INTERACTION
??

## Slide 19
  Building – envelope & systems
  Furnishings
  – functional, ornamental
  Occupants
  – people, plants,
  pets, pests
  Indoor activities
  – daily living, recreational
Contaminant Sources

## Slide 20: Gases:
Outdoor Sources
Combustion Products

## Slide 21: Outdoor Sources & Building Design
Air Intakes
- rooftop
- parking garage

## Slide 22: Radon
Radon is a gaseous, colorless, highly toxic radioactive element
Sources: earth and rock beneath home; well water; building materials
Health effect: lung cancer
Notes: 22
Heating and Cooling Systems are designed to provides thermal comfort. Thermal comfort does not have a universal definition and is therefore defined by the satisfaction of inhabitants.

## Slide 23: Combustion - Carbon Monoxide
Colorless, odorless gas produced by incomplete combustion of a fuel containing carbon
Combines with hemoglobin, replacing oxygen
Symptoms
  Headache, Fatigue
  Shortness of breath
  Nausea, Dizziness
Most common sources
  house fires
  heaters
  car exhaust
Common problems
  heater maintenance
  insufficient air supply
  unintended air pathways
Notes: 23
Heating and Cooling Systems are designed to provides thermal comfort. Thermal comfort does not have a universal definition and is therefore defined by the satisfaction of inhabitants.

## Slide 24: Combustion - Oxides of Nitrogen (NOx)
Produced by high-temperature combustion
Sources
  gas stoves
  heaters
  car exhaust
Health effects
  respiratory
  asthma
Indoor NO2 levels are function of:
  indoor sources
  pilot lights
  exhaust/range hood
  usage pattern
  outdoor levels
  size of home
  ventilation rate
  humidity
Notes: 24
Heating and Cooling Systems are designed to provides thermal comfort. Thermal comfort does not have a universal definition and is therefore defined by the satisfaction of inhabitants.

## Slide 25: Chemicals:
Formaldehyde
Volatile Organic Compounds (VOCs)

## Slide 26: Product Offgassing
Amount, type, concentration
Depends on…
  Type of material
  Age
  Temperature and humidity
  Absorbtion/desorption
  Ventilation/air concentration

## Slide 27: Sources of Formaldehyde

## Slide 28: VOCs
"volatile organic compound" - carbon-containing chemicals that are gases at room temperature
Semi-volatile organic compounds (SVOCs) are present partly as gaseous airborne chemicals and partly as chemicals adsorbed on indoor surfaces and microscopic airborne and settled particles.
Sources: building materials, furnishings, cleaning compounds, office equipment, personal care products, air fresheners, pesticides, people, and unvented combustion processes such as tobacco smoking or cooking with gas stoves
suspected health effects may include sensory irritation symptoms, allergies and asthma, neurological and liver toxicity, and cancer

## Slide 29: Sources of VOCs
Materials
Paints, varnish
Plastics
Dry cleaning
Cleaning Supplies
Flooring Material

## Slide 30: Offgassing - decay curve
2 weeks

## Slide 31: Particulates:
Dust
Smoke
Aerosols

## Slide 32: Particle Sources
Smoking
Cooking
Occupants
Outside Dust

## Slide 33: Particle Sizes: PM2.5 , PM10

## Slide 34: Why Size DOES matter!

## Slide 35: Asbestos
Asbestos is a mineral fiber
Used in over 3000 materials
  asbestos-cement products
  ceiling and floor tiles
  insulation
  brakes
Health effects
  lung cancer (mesothelioma)
All new uses banned by EPA in 1989
Notes: 35
Heating and Cooling Systems are designed to provides thermal comfort. Thermal comfort does not have a universal definition and is therefore defined by the satisfaction of inhabitants.

## Slide 36: Allergens:
Elicit an allergic reaction in sensitive individuals
Usually biological in nature

## Slide 37: Allergens
Living microorganisms
(e.g. fungi, bacteria, viruses)
Particles & fragments of organisms
(e.g. pollen, spores, mycelia, endotoxin)
Particulate waste products
(e.g. pet dander, dust mite fecal pellets)
Metabolic products
(e.g. mycotoxins, microbial VOCs)

## Slide 38: Pollen
Mainly outdoor plants
Seasonal
Generally large (>10 m)
Notes: 38
Heating and Cooling Systems are designed to provides thermal comfort. Thermal comfort does not have a universal definition and is therefore defined by the satisfaction of inhabitants.

## Slide 40
Air Quality
  Gases
  Chemicals/fumes (VOCs)
  Particulates
  Allergens
Thermal Comfort
  Temperature
  Humidity
Occupants
Building/Systems
INTERACTION
??

## Slide 41
Occupants (exhaled)
Activities (cook, shower)
Water-related Utilities
Building Envelope
Humidity/Cold Surfaces
Moisture Sources

## Slide 42: Name That Source & Type!!
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20

## Slide 43: Who has control over sources?
Builders??
Homeowners??

## Slide 44: Who has control over sources?

## Slide 45: Building Envelope and Systems are KEY to good IEQ
Buildings are “too” tight:
  Moisture accumulation
  Contaminant accumulation
  Thermal discomfort
Uncontrolled air exchange:
  Contaminant source
  Contaminant migration from unconditioned spaces
  Drafts
  Energy loss
Inadequate or spotty insulation
  Cold condensing surfaces
  Energy Loss