## Slide 1: Part 3: Keeping Homes Healthy
Dr. Susan Doll

## Slide 2: IAQ is Important
Americans spend 90% of their day indoors – in classrooms, offices, commercial buildings, at home.
Airborne chemicals indoors are often at least two to five times higher than outdoors.
Airborne microbial populations can be different and amplified relative to outdoor populations.
When compared to other threats to human health, the EPA Science Advisory Board consistently ranks indoor air pollution among the top 4 environmental risks facing Americans.

## Slide 3: Standards for Air Quality
Contaminants
  EPA (outdoors)
  NAQS
  OSHA: occupational,
  high exposure/short time
  PEL - Permissible Exposure Level (1 hour, 8-hour, lifetime limits)
  WHO (World Health Organization)
  ASHRAE (CO2 surrogate)
Thermal Comfort – ASHRAE

## Slide 4
  Symptoms linked to building
  Resolve when not in building
  Effect a substantial fraction of occupants
Non-Specific Symptoms
Dry, itchy eyes
Nasal irritation
Hoarseness, irritated throat, laryngitis
Skin problems
Fuzzy thinking, memory
Irritability, sleep disruption, fatigue
Headaches, nausea
Sick Building Syndrome

## Slide 5
  Discrete identifiable disease or illness
  Can be traced to specific source within a building
Examples:
asthma exacerbation
Legionnaires’ disease
hypersensitivity pneumonitis
carbon monoxide poisoning
Building-Related Illness

## Slide 6: Pathway to Disease
OUTCOME
SOURCE
What happens in between?
Who gets sick and why?

## Slide 7: Pathway to Disease
  Materials, people, pets, activities => generated indoors/outdoors (gases, chemicals, particles, allergens)
  Airborne contaminants => concentration in air over time
  (diffusion, aerosolization, convection/contain, decay)
  Inhalation, contact => time spent indoors + activities
  (proximity, breathing rate)
  Recipient => Adverse Health Effects
  (age, immune status, genetics)
SOURCE
EXPOSURE
OUTCOME
DISPERSAL

## Slide 8: REDUCE - low VOC products

## Slide 9: REDUCE – vent to outside
WATER HEATER
POTTERY KILN

## Slide 10: Ways to Reduce Health Impact
SOURCE
DISPERSAL
EXPOSURE
OUTCOME
1
2
MAKE LESS - use a better widget, stop doing it
EMIT LESS INDOORS – control emission at source, chimney, vacuum
3
4
DILUTE – Passive (windows, doors, vents) Active (fan)
REMOVE FROM AIR – filter, absorbent

## Slide 11
Heating, ventilation, and air conditioning systems (HVAC)
Supply mixture of outdoor and recirculated indoor air that has been filtered and thermally conditioned
“Natural” ventilation (i.e. windows)
DILUTE - Ventilation

## Slide 12
REMOVE – particles
Standard
Pleated
Electronic
Intense field
dielectric
HEPA
Ionic

## Slide 13
REMOVE – all types

## Slide 14: Ways to Reduce Health Impact
SOURCE
DISPERSAL
EXPOSURE
OUTCOME
1
2
MAKE LESS - use a better widget, stop doing it
EMIT LESS INDOORS – control emission at source, chimney, vacuum
3
4
5
6
DILUTE – Passive (windows, doors, vents) Active (fan)
REMOVE FROM AIR – filter, scrubber
AVOID - reduce time in exposure area
PROTECT – reduce contact or inhalation (mask, gloves)

## Slide 15: Limiting Exposure
Dedicated/Separate Workspace
Personal Protective Equipment (PPE)

## Slide 16: Ways to Reduce Health Impact
SOURCE
DISPERSAL
EXPOSURE
OUTCOME
1
2
MAKE LESS - use a better widget, stop doing it
EMIT LESS INDOORS – control emission at source, chimney, vacuum
3
4
5
6
DILUTE – Passive (windows, doors, vents) Active (fan)
REMOVE FROM AIR – filter, scrubber
REDUCE RISK - Improve general health conditions, early and effective treatment, identify source
7
AVOID - reduce time in exposure area
PROTECT – reduce contact or inhalation (mask, gloves)

## Slide 17: Reduce Risk
Vulnerable Populations
Early Warning Monitors

## Slide 19
SOURCE
DISPERSAL
EXPOSURE
OUTCOME
1
2
MAKE LESS - use a better widget, stop doing it
EMIT LESS INDOORS – control emission at source, chimney, vacuum
3
4
5
6
DILUTE – Passive (windows, doors, vents) Active (fan)
REMOVE FROM AIR – filter, scrubber
AVOID - reduce time in exposure area
PROTECT – reduce contact or inhalation (mask, gloves)
RADON: a special case
(known carcinogen)

## Slide 20
RADON – prevention

## Slide 21
RADON – dilution
Heat Recovery Ventilator

## Slide 22
Air Quality
  Gases
  Chemicals/fumes (VOCs)
  Particulates
  Allergens
Thermal Comfort
  Temperature
  Humidity
SOURCE
DISPERSAL
EXPOSURE
OUTCOME

## Slide 23: OPPORTUNISTIC Sources
Proliferate in Favorable Environments:
Rodents – gaps in envelope
Cockroaches – ready food source
Bacteria – standing water
Dust Mites – skin scales, high humidity
Fungi – moisture, substrate

## Slide 24
Fungal Growth Requirements
Nutrients
Temperature
Moisture

## Slide 25: Indoor Environments
Indoor surfaces can support fungal growth by providing
  sufficient oxygen
  suitable temperatures
  source of nutrition
  moisture
MOISTURE CONTROL IS KEY !

## Slide 26: Mold (fungi)
Naturally occurring single-cell organisms
Found in all environments at some levels
In the right conditions mold multiplies, forms colonies, and sporulates

## Slide 27: Agents of disease produced by molds
Glucans
Allergens
Toxins
Gases
Spore

## Slide 28: Human Health Effects
Allergic
  Asthma trigger (possible promoter)
  Damp/moldy homes lead to respiratory system illnesses in children
Irritant
  Mucous membrane (eyes, nose, throat) irritation and may lead to headaches
Notes: 28

## Slide 29: Human Health Effects (cont.)
Infectious
  Healthy people are only affected by a few infectious fungi
  Immuno-compromised susceptibility
Toxic
  Mycotoxicoses
    Toxic effects well documented related to ingestion
    Some evidence in agricultural settings
    Lack of evidence between disease and mycotoxin exposure in homes or offices
Notes: 29

## Slide 30: Toxic Mold?
“The hazards presented by molds that may contain mycotoxins should be considered the same as other common molds. . . There are very few case reports that toxic molds. . . can cause unique or rare health conditions such as pulmonary hemorrhage or memory loss. These case reports are rare, and a causal link between the presence of the toxic mold and these conditions has not been proven.”
-- US Center for Disease Control
Notes: http://www.cdc.gov/nceh/airpollution/mold/stachy.htm#Q14

## Slide 31
Occupants (exhaled)
Activities (cook, shower)
Water-related Utilities
Building Envelope
Humidity/Cold Surfaces
Moisture Sources

## Slide 32: Moisture capacity of homes
100 years ago with masonry walls houses could hold 500 gls of water
50 years ago wood houses could hold 100 gls of water
Today metal studs, gypsum, & vinyl can hold 50 – 5 gls of water

## Slide 33
When is high humidity a problem?
If a material gets wet, how long before it gets moldy?
What role do material properties play in development and prevention of mold growth?
Key Questions

## Slide 34
Wallboard (W)
Plywood (P)
Ceiling Tile (CT)
Oriented Strand Board
(OSB)

## Slide 35
Number of Samples
Moisture Content W CT P OSB
  5 mg/cm3 (75%RH) 2 2 - -
  7 mg/cm3 (85%RH) 2 2 - -
  10 mg/cm3 (95%RH) 2 2 - -
  15 mg/cm3 (~100%RH) 2 2 - -
  50 mg/cm3 2 2 2 2 (75%RH)
  75 mg/cm3 2 2 2 2 (85%RH)
  100 mg/cm3 - 2 2 2 (95%RH)
  150 mg/cm3 2 2 2 2 (~100%RH)
  200 mg/cm3 - - 2 2
  250 mg/cm3 2 2 2 2
  300 mg/cm3 - - 2 2
  350 mg/cm3 2 2 2 2
Test Conditions

## Slide 36
Temperature control
  (+/- 0.2 °C)

## Slide 37: Fungal Growth Evaluation
In-situ observation
  Examine surfaces @ 20X magnification
  Record observations on grid data sheet
  => morphology
  => area coverage
N = 150 samples

## Slide 38: When“moisture” is a problem
Liquid water is necessary (growth in days)
    Condensation
    Leaks
    Floods
    Spills
Very few fungi will grow with only equilibrium moisture from the air, then only if RH is >95%. (growth in weeks to months)

## Slide 39: Role of Materials
What kind of ‘food’ is available for growth
Moisture retention properties
Location

## Slide 40: Potential High Risk Areas
Materials with organic content
Cool subgrade and exterior surfaces
Materials under/behind furniture or built-in cabinetry, sub flooring
Surfaces behind impermeable finishing materials
Horizontal surfaces where pooling may occur
Cavities where moisture can accumulate

## Slide 41: Faulty HVAC installation

## Slide 42: Building Systems - Leaking Pipes

## Slide 43: Exterior Details
Landscaping
sprinkler lines
Caulking
failures

## Slide 44: Roof Design
Ice dams
Flat roofs

## Slide 45: Unconditioned Subgrade Spaces

## Slide 46: Sub Flooring

## Slide 47: Impervious Wall Coverings

## Slide 48: Insulated Wall Cavities

## Slide 49: How to prevent mold growth
Ventilate moisture at source
Repair leaks as they occur
Clean up water from floods quickly
Prevent ground water intrusion
Insulate to prevent cold surfaces
Dehumidify where appropriate
Limit use of humidifiers
Appropriate materials
Vent Fans

## Slide 50: Moisture Resistant Materials - FLOORING
Concrete materials: tile, pre-cast concrete, or latex or bituminous formed-in-place (can be colored, polished, and sealed)
Non-porous stone, slate, or cast stone with waterproof mortar (may inhibit drying of the subfloor).
Clay tile, quarry tile, terrazzo, or ceramic tile
Rubber sheets or tiles
Solid plastic lumber (may inhibit drying)

## Slide 51: Moisture Resistant Materials - WALLS
Steel with waterproof applications (coated to resist corrosion); steel studs, beams, and sill plates.
Solid naturally decay-resistant wood for structural components.
Mineral - Brick , Concrete, Natural solid, veneer, or cast stone with waterproof grout
Tile - Structural glazed clay tile, Ceramic veneer or ceramic wall tile
Glass blocks or glass panels (may break)
Plaster with metal lath
Rubber mold epoxy polyamide adhesive or latex hydraulic cement
Non paper-faced gypsum wallboard - water resistant fiber-reinforced gypsum wallboard or panels, or cement board

## Slide 52: If you still get mold...
BASIC RULES FOR CLEANUP:
Identify and eliminate moisture source
  - prevent reoccurrence
Use appropriate PPE & containment
  - protect health of occupants & workers
  - prevent spread of contamination
Remediate damaged materials
  - repair structural damage
  - remove source of mold growth

## Slide 53: Water-Damaged Materials
Response to clean water damage within 24-48 hours to prevent mold growth
Accelerate drying process with dehumidifiers, fans, and/or heaters*
Remove wet materials that are unlikely to dry

## Slide 54: Mold Remediation Protocols
New York City Department of Public Health “Guidelines on Assessment and Remediation of Fungi in Indoor Environments” http://www.ci.nyc.ny.us/html/doh/html/epi/moldrpt1.html
US EPA
“Mold Remediation in Schools and Public Buildings” http://www.epa.gov/iaq/molds/mold_remediation.html

## Slide 55: 7 Healthy Homes Principles
Keep It:
Dry
Clean
Ventilated
Pest-Free
Safe
Contaminant-Free
Maintained
Anything airborne
Particles, allergens
Mold, allergens
Particles, allergens
ALL
ALL
What’s missing/assumed for these principles?
Notes: While there is no recipe that can guarantee a healthy home, you’ll be learning about key principles that can help create healthier indoor environments. You’ll hear about these principles throughout the course of the training.
In this training, we are introducing a new way of thinking about the home environment – an approach that considers the people living in the home, the building itself, and the potential health problems.