## Slide 1: Part 3: Keeping Homes Healthy
Dr. Susan Doll

## Slide 2: 7 Healthy Homes Principles
Keep It:
Dry
Clean
Ventilated
Pest-Free
Safe
Contaminant-Free
Maintained
Notes: While there is no recipe that can guarantee a healthy home, you’ll be learning about key principles that can help create healthier indoor environments. You’ll hear about these principles throughout the course of the training.
In this training, we are introducing a new way of thinking about the home environment – an approach that considers the people living in the home, the building itself, and the potential health problems.

## Slide 3: 7 Healthy Homes Principles
Keep It:
Dry
Clean
Ventilated
Pest-Free
Safe
Contaminant-Free
Maintained
Notes: While there is no recipe that can guarantee a healthy home, you’ll be learning about key principles that can help create healthier indoor environments. You’ll hear about these principles throughout the course of the training.
In this training, we are introducing a new way of thinking about the home environment – an approach that considers the people living in the home, the building itself, and the potential health problems.

## Slide 4: IAQ is Important
Americans spend 90% of their day indoors – in classrooms, offices, commercial buildings, at home.
Airborne chemicals indoors are often at least two to five times higher than outdoors.
Airborne microbial populations can be different and amplified relative to outdoor populations.
When compared to other threats to human health, the EPA Science Advisory Board consistently ranks indoor air pollution among the top 4 environmental risks facing Americans.

## Slide 5: Standards for Air Quality
Contaminants
  EPA (outdoors)
  NAQS
  OSHA: occupational,
  high exposure/short time
  PEL - Permissible Exposure Level
  (1 hour, 8-hour, lifetime limits)
  WHO (World Health Oranization)
  ASHRAE (CO2 surrogate)
Thermal Comfort - ASHRAE

## Slide 6
  Symptoms linked to building
  Resolve when not in building
  Effect a substantial fraction of occupants
Non-Specific Symptoms
Dry, itchy eyes
Nasal irritation
Hoarseness, irritated throat, laryngitis
Skin problems
Fuzzy thinking, memory
Irritability, sleep disruption, fatigue
Headaches, nausea
Sick Building Syndrome

## Slide 7
  Discrete identifiable disease or illness
  Can be traced to specific source within a building
Examples:
asthma exacerbation
Legionnaires’ disease
hypersensitivity pneumonitis
carbon monoxide poisoning
Building-Related Illness

## Slide 8: Pathway to Disease
SOURCE
DISPERSAL
EXPOSURE
OUTCOME

## Slide 9: Pathway to Disease
  Materials, people, pets, activities => generated indoors/outdoors
  gases, chemicals, particles, allergens
SOURCE
DISPERSAL
EXPOSURE
OUTCOME

## Slide 10: Pathway to Disease
  Materials, people, pets, activities => generated indoors/outdoors
  gases, chemicals, particles, allergens
  Airborne contaminants => concentration in air over time
  diffusion, aerosolization, convection/contain, decay
SOURCE
DISPERSAL
EXPOSURE
OUTCOME

## Slide 11: Pathway to Disease
  Materials, people, pets, activities => generated indoors/outdoors
  gases, chemicals, particles, allergens
  Airborne contaminants => concentration in air over time
  diffusion, aerosolization, convection/contain, decay
  Inhalation, contact => time spent indoors + activities
  proximity, breathing rate
SOURCE
DISPERSAL
EXPOSURE
OUTCOME

## Slide 12: Pathway to Disease
  Materials, people, pets, activities => generated indoors/outdoors
  gases, chemicals, particles, allergens
  Airborne contaminants => concentration in air over time
  diffusion, aerosolization, convection/contain, decay
  Inhalation, contact => time spent indoors + activities
  proximity, breathing rate
  Recipient => Adverse Health Effects
  age, immune status, genetics
SOURCE
DISPERSAL
EXPOSURE
OUTCOME

## Slide 13: Ways to Reduce Health Impact
SOURCE
DISPERSAL
EXPOSURE
OUTCOME
1
2
MAKE LESS - use a better product, stop doing it
EMIT LESS INDOORS – control emission at source, chimney/vent

## Slide 14: REDUCE - low VOC products

## Slide 15: REDUCE – vent to outside
WATER HEATER
POTTERY KILN

## Slide 16: Ways to Reduce Health Impact
SOURCE
DISPERSAL
EXPOSURE
OUTCOME
1
2
MAKE LESS - use a better widget, stop doing it
EMIT LESS INDOORS – control emission at source, chimney, vacuum
3
4
DILUTE – Passive (windows, doors, vents) Active (fan)
REMOVE FROM AIR – filter, absorbent

## Slide 17
Heating, ventilation, and air conditioning systems (HVAC)
Supply mixture of outdoor and recirculated indoor air that has been filtered and thermally conditioned
“Natural” ventilation (i.e. windows)
DILUTE - Ventilation

## Slide 18
REMOVE – particles
Standard
Pleated
Electronic
Intense field
dielectric
HEPA
Ionic

## Slide 19
REMOVE – all types

## Slide 20: Ways to Reduce Health Impact
SOURCE
DISPERSAL
EXPOSURE
OUTCOME
1
2
MAKE LESS - use a better widget, stop doing it
EMIT LESS INDOORS – control emission at source, chimney, vacuum
3
4
5
6
DILUTE – Passive (windows, doors, vents) Active (fan)
REMOVE FROM AIR – filter, scrubber
AVOID - reduce time in exposure area
PROTECT – reduce contact or inhalation (mask, gloves)

## Slide 21: Limiting Exposure
Dedicated/Separate Workspace
Personal Protective Equipment (PPE)

## Slide 22: Ways to Reduce Health Impact
SOURCE
DISPERSAL
EXPOSURE
OUTCOME
1
2
MAKE LESS - use a better widget, stop doing it
EMIT LESS INDOORS – control emission at source, chimney, vacuum
3
4
5
6
DILUTE – Passive (windows, doors, vents) Active (fan)
REMOVE FROM AIR – filter, scrubber
REDUCE RISK - Improve general health conditions, early and effective treatment, identify source
7
AVOID - reduce time in exposure area
PROTECT – reduce contact or inhalation (mask, gloves)

## Slide 23: Reduce Risk
Vulnerable Populations
Early Warning Monitors

## Slide 24
SOURCE
DISPERSAL
EXPOSURE
OUTCOME
1
2
MAKE LESS - use a better widget, stop doing it
EMIT LESS INDOORS – control emission at source, chimney, vacuum
3
4
5
6
DILUTE – Passive (windows, doors, vents) Active (fan)
REMOVE FROM AIR – filter, scrubber
AVOID - reduce time in exposure area
PROTECT – reduce contact or inhalation (mask, gloves)
RADON – a special case

## Slide 25
RADON – ventilation

## Slide 26
RADON – prevention

## Slide 27: 7 Healthy Homes Principles
Keep It:
Dry
Clean
Ventilated
Pest-Free
Safe
Contaminant-Free
Maintained
Notes: While there is no recipe that can guarantee a healthy home, you’ll be learning about key principles that can help create healthier indoor environments. You’ll hear about these principles throughout the course of the training.
In this training, we are introducing a new way of thinking about the home environment – an approach that considers the people living in the home, the building itself, and the potential health problems.

## Slide 28
Air Quality
  Gases
  Chemicals/fumes (VOCs)
  Particulates
  Allergens
Thermal Comfort
  Temperature
  Humidity
SOURCE
DISPERSAL
EXPOSURE
OUTCOME

## Slide 29: OPPORTUNISTIC Sources
Proliferate in Favorable Environments:
Rodents – gaps in envelope
Cockroaches – ready food source
Bacteria – standing water
Dust Mites – skin scales, high humidity
Fungi – moisture, substrate

## Slide 30
Fungal Growth Requirements
Nutrients
Temperature
Moisture

## Slide 31: Indoor Environments
Indoor surfaces can support fungal growth by providing
  sufficient oxygen
  suitable temperatures
  source of nutrition
  moisture
MOISTURE CONTROL IS KEY !

## Slide 32: 7 Healthy Homes Principles
Keep It:
Dry
Clean
Ventilated
Pest-Free
Safe
Contaminant-Free
Maintained
Notes: While there is no recipe that can guarantee a healthy home, you’ll be learning about key principles that can help create healthier indoor environments. You’ll hear about these principles throughout the course of the training.
In this training, we are introducing a new way of thinking about the home environment – an approach that considers the people living in the home, the building itself, and the potential health problems.

## Slide 33: Mold (fungi)
Naturally occurring single-cell organisms
Found in all environments at some levels
In the right conditions mold multiplies, forms colonies, and sporulates

## Slide 34: Agents of disease produced by molds
Glucans
Allergens
Toxins
Gases
Spore

## Slide 35: Human Health Effects
Allergic
  Asthma trigger (possible promoter)
  Damp/moldy homes lead to respiratory system illnesses in children
Irritant
  Mucous membrane (eyes, nose, throat) irritation and may lead to headaches
Notes: 35

## Slide 36: Human Health Effects (cont.)
Infectious
  Healthy people are only affected by a few infectious fungi
  Immuno-compromised susceptibility
Toxic
  Mycotoxicoses
    Toxic effects well documented related to ingestion
    Some evidence in agricultural settings
    Lack of evidence between disease and mycotoxin exposure in homes or offices
Notes: 36

## Slide 37: Toxic Mold?
“The hazards presented by molds that may contain mycotoxins should be considered the same as other common molds. . . There are very few case reports that toxic molds. . . can cause unique or rare health conditions such as pulmonary hemorrhage or memory loss. These case reports are rare, and a causal link between the presence of the toxic mold and these conditions has not been proven.”
-- US Center for Disease Control
Notes: http://www.cdc.gov/nceh/airpollution/mold/stachy.htm#Q14

## Slide 38
Occupants (exhaled)
Activities (cook, shower)
Water-related Utilities
Building Envelope
Humidity/Cold Surfaces
Moisture Sources

## Slide 39: Moisture capacity of homes
100 years ago with masonry walls houses could hold 500 gls of water
50 years ago wood houses could hold 100 gls of water
Today metal studs, gypsum, & vinyl can hold 50 – 5 gls of water

## Slide 40
When is high humidity a problem?
If a material gets wet, how long before it gets moldy?
What role do material properties play in development and prevention of mold growth?
Key Questions

## Slide 41
Wallboard (W)
Plywood (P)
Ceiling Tile (CT)
Oriented Strand Board
(OSB)

## Slide 42
Number of Samples
Moisture Content W CT P OSB
  5 mg/cm3 (75%RH) 2 2 - -
  7 mg/cm3 (85%RH) 2 2 - -
  10 mg/cm3 (95%RH) 2 2 - -
  15 mg/cm3 (~100%RH) 2 2 - -
  50 mg/cm3 2 2 2 2 (75%RH)
  75 mg/cm3 2 2 2 2 (85%RH)
  100 mg/cm3 - 2 2 2 (95%RH)
  150 mg/cm3 2 2 2 2 (~100%RH)
  200 mg/cm3 - - 2 2
  250 mg/cm3 2 2 2 2
  300 mg/cm3 - - 2 2
  350 mg/cm3 2 2 2 2
Test Conditions

## Slide 43
Temperature control
  (+/- 0.2 °C)

## Slide 44: Fungal Growth Evaluation
In-situ observation
  Examine surfaces @ 20X magnification
  Record observations on grid data sheet
  => morphology
  => area coverage
N = 150 samples

## Slide 45: When“moisture” is a problem
Liquid water is necessary (growth in days)
    Condensation
    Leaks
    Floods
    Spills
Very few fungi will grow with only equilibrium moisture from the air, then only if RH is >95%. (growth in weeks to months)

## Slide 46: Potential High Risk Areas
Materials with organic content
Cool subgrade and exterior surfaces
Materials under/behind furniture or built-in cabinetry, sub flooring
Surfaces behind impermeable finishing materials
Horizontal surfaces where pooling may occur
Cavities where moisture can accumulate

## Slide 47: Faulty HVAC installation

## Slide 48: Building Systems - Leaking Pipes

## Slide 49: Exterior Details
Landscaping
sprinkler lines
Caulking
failures

## Slide 50: Roof Design
Ice dams
Flat roofs

## Slide 51: Unconditioned Subgrade Spaces

## Slide 52: Sub Flooring

## Slide 53: Impervious Wall Coverings

## Slide 54: Insulated Wall Cavities

## Slide 55: How to prevent mold growth
Ventilate moisture at source
Repair leaks as they occur
Clean up water from floods quickly
Prevent ground water intrusion
Insulate to prevent cold surfaces
Dehumidify where appropriate
Limit use of humidifiers
Appropriate materials
Vent Fans

## Slide 56: 7 Healthy Homes Principles
Keep It:
Dry
Clean
Ventilated
Pest-Free
Safe
Contaminant-Free
Maintained
Notes: While there is no recipe that can guarantee a healthy home, you’ll be learning about key principles that can help create healthier indoor environments. You’ll hear about these principles throughout the course of the training.
In this training, we are introducing a new way of thinking about the home environment – an approach that considers the people living in the home, the building itself, and the potential health problems.