## Slide 1
Solar Site Assessment

## Slide 2: Why the variation in solar radiation?
Amount of atmosphere sun’s energy must travel through to reach earth
  Time of day, Time of year, tilt of earth
Cloudiness
Shading

## Slide 4: NC SOLAR RESOURCE
Other Cities for Comparison | 
Miami, FL | 5.2
Albany, NY | 4.3
Phoenix, AZ | 6.5
Tokyo | 4.5
Berlin | 3.0

## Slide 7
SUMMER SOLSTICE NORTHERN HEMISPHERE

## Slide 8: Solar Trajectory
2-3
Solar Resources - Solar Radiation
Notes: Trajectories of the Sun
As a result of the relative movements of the Earth and the Sun, the Sun appears to a given point on the Earth on the horizon (sunrise) as shown in the illustration, rises on the celestial sphere up to maximum height and thereafter declines until again reaching the horizon (sunset). This happens every day of the year with different trajectories between the winter solstice (21 December) and summer solstice (21 June) passing through the vernal (21 March) and autumnal (21 September) equinoxes. On any day of the year, the Sun is found between these two outermost trajectories.
The maximum height of the Sun can be calculated fairly easily:
equinoxes: 90° - latitude
solstices: (90° - latitude) +/- 23°27’’
other days: (90° - latitude) +/- solar declination

## Slide 13: General Siting Guidelines
Face Collectors towards the south
Year round performance will be greatest if collectors tilted at angle of latitude (36 degrees)
Summer Lat – 15
Winter Lat + 15
Clear of shading from
9 – 3

## Slide 14: Tilt Angles & Roof Pitch
Roof Pitch | Tilt Angle (°)
4/12 | 18.4
5/12 | 22.6
6/12 | 26.6
7/12 | 30.3
8/12 | 33.7
9/12 | 36.9
10/12 | 39.8
11/12 | 42.5
12/12 | 45.0

## Slide 15: Do We Have to Face Exactly South?
Raleigh NC 35.9º Latitude

## Slide 16: So What About Slope?
Raleigh, NC 35.9 deg Latitude 14 deg => 95% of Maximum

## Slide 17: Orientation Effect on Annual Output

## Slide 18: Shading can reduce performance significantly

## Slide 19: Types of Solar Site Assessments
1. Compass, Protractor with Weighted String and Sun Chart Method
All you need is a pencil, sun chart, compass, and a protractor with a weighted string.
http://solardat.uoregon.edu/SunChartProgram.html

## Slide 26: Compass and Protractor Method
Stand at the proposed site.
Face south, adjusting for magnetic declination
Point the flat end of the protractor at the horizon or any other obstructions (trees, buildings, etc.)
Measure the number of degrees the string is off from 90 degrees.
Record findings on Sun chart.
Repeat process in 15 degree increments for both East and West.
Connect horizon dots and see if any hours are obstructed for any months between the hours of 9a – 3p.

## Slide 29: Magnetic Declination
Magnetic declination is the deviation of magnetic north from true north or how much and in what direction the compass needle is off of true north.
    True south in western NC is approximately 7 degrees west of magnetic south

## Slide 30: Magnetic Declination in the U.S.

## Slide 31: Using the Solar Pathfinder

## Slide 32: Pathfinder on Roof

## Slide 33: Solar Pathfinder
http://www.solarpathfinder.com/video

## Slide 37: Solmetric Suneye
http://www.youtube.com/watch?v=JDgtYEQLdxw

## Slide 38: Extension Kit

## Slide 39: Solmetric PV Designer
http://www.solmetric.com/buy210.html
http://www.solmetric.com/

## Slide 40: Solmetric PV Designer